## Slide 1: Standardizing AI Lung Nodule Reporting into DICOM-Compatible Annotations for Rapid Visualization.
Zachary Wong, SSRP Summer Student

## Slide 2: Project goal
Input segmentations/bounding boxes measured by AI systems into DICOM format
AI systems (Cirrus, Sybil etc) often output into csv and other non-DICOM format
Why is DICOM (Digitial Imaging and Communications in Medicine) format important?
Rigid, standardized structure -> less ambiguity and error
Universally recognized by clinicians and medical systems -> good interoperability
Lots of metadata -> accurate interpretation
DICOM
file.dcm
Portable Document Format
file.pdf
Comma Separated Values
file.csv

## Slide 3: Project goal
Existing DICOM
Cirrus csv
New DICOM with annotations (annotations in SR format)
+

## Slide 4: Project Components
Four components of project:
Find relevant dicoms using cirrus outputs (study, relevant slices of ROI, kernel)
Create annotation as segmentation mask to be inputted in SR file
Track uids for input/later reference through sql database
Incorporates everything into SR file output for CT storage

## Slide 5: Finding relevant dicoms
Each filter searches for a match between dicom and cirrus csv
DICOM | Cirrus CSV
Study UID | Study UID
Instance number (different instance per slice) | Slice number +- diameter
Reconstruction kernel | Convolution kernel
**Study UID is not currently present in cirrus cleaned output but this can probably be easily changed

## Slide 6: Creating annotations
Criteria for annotations
Annotations must be in the correct coordinate system
Annotations must be accepted by dicom SR (structured report) format
Coordinate systems:
Voxel coordinates: location of voxel (3d pixel) relative to image grid
World coordinates: physical coordinates in 3d space expressed in mm
Coordinate conversion is necessary for some annotations

## Slide 7: Valid SR Annotations
Annotation | Process | Benefits/Detriments
Point (world) | Take nodule center directly from cirrus -> output into sr | Ensures accuracy since no extra calculations/conversions needed
Ellipsoid (world) | Compute ellipsoid -> output into sr | SR file is vector (saves loading time + disc space) but NOT visualizable with program
Segmentation (voxel) | Compute ellipsoid -> translate into voxel units -> create seg mask -> output into sr | Accurate segmentation outputs can be potentially easily incorporated into workflow
Polyline (world) | Compute 3d box -> output into sr | Box in this format cannot “close” to surround a volume
Polygon (world) | Compute 3d boxes (one for each slice) -> output into sr | Not a clean SR file having multiple boxes
**Annotations that my engine will complete; one sr file may have multiple annotations

## Slide 8: Annotation creation process
Ellipsoid is built
X, y, z of nodule center is given (world coord)
X and y of ellipsoid is computed using major axis for both (cirrus doesn’t specify orientation of major axis)
Z of ellipsoid is computed using diameter (assuming all scans are axial, feet first)
For segmentations, ellipsoid converted into voxel coord
Uses patient position, pixel spacing, and slice thickness outputs from cirrus
Can potentially use patient orientation from dicom IF they are non axial
Voxel coord ellipsoid is converted into segmentation mask
Segmentation mask is outputted to be later referenced

## Slide 9: UID Structure
What is a UID (Unique Identifier)?
Long string of numbers and decimals unique to an object allowing object to be identified
Following structure rigidly allows for references to objects/series without confusion
Example: 1.2.124.113532.142.71.190.136.20090416.103812.15148805
Four types of UIDs we need to consider:
Study UID
Series UID
SOP (service object pair)
Tracking UID (for segmentation/sr objects only)

## Slide 10: UID Structure
Study UID (ex. 1.2.124.113532.142.71.190.136.20090416.103812.15148805)
CT Scan Series UID
Segmentation Series UID
SR Series UID
Slice 1 SOP UID
Slice 3 SOP UID
Slice 2 SOP UID
Unique SOP UID per segmentation
Unique SOP UID per SR object
Red text = UID needs to be generated by engine
Black text = UID exists already and needs to be stored by engine

## Slide 11: UID Tracker Database

## Slide 12: UID Tracker Database
Database functions:
Need to be able to save new generated UIDs for series/SOP objects
Need to be able to fetch old UIDs (ex. series UIDs, tracking UIDs)
How to implement above functions?
Use a key and value dictionary system using sql
Find tracking UIDs using patient + nodule ID
Find series UIDs using study UID

## Slide 13: UID Tracker Database

## Slide 14: Output
Uses highdicom package (open source, python, 2022) to more easily package metadata into dicom format

## Slide 15: Output
Segmentation and sr files are perhaps to be outputted in same folder as study with all other CT images

## Slide 16: Output
When you click on a study in 3D slicer something like this should appear

## Slide 17: Output – Metadata in 3D slicer
Data is accurately inputted, along with tags and UIDs that should match database

## Slide 18: Output – Images in 3D slicer
Segmentation masks should be small relative to size of image

## Slide 19: Output – Images in 3D slicer

## Slide 20: Project directions
Finish segmentation so that it appears in slicer
Output a point within the SR file additional to the segmentation and sr file
Most folder paths are currently hard coded.. Code parse-able paths
Dictionary with variable names/column names should be created in case cirrus outputs change, etc
Currently, DICOMs are filtered by their attributes, but they should be filtered by tags for more consistency
Clean up code and variable names for consistency